## Slide 1
Direct driving the QUAD
ESL 989 electrostatic speaker
Jan Didden
ETF 2022, Baarlo, The Netherlands

## Slide 2
Lifelong fascination with audio electronics
Writing for Wireless World, ELRAD,
Costruire HiFi, Audio Amateur, Elektor, L’Audiophile
Chairman NL-section AES, AES Life member
Presentations at AES, RMAF, ETF, Burning Amp, YouTube channel
One patent on Error Correction
Publisher/Editor Linear Audio bookzine
Technical Editor AudioXpress
Where I am coming from

## Slide 3
An ESL 63/989 primer
Direct drive – why bother?
Requirements – voltage, current, freq. response
Design considerations
Realization – schematics, system diagram
Software features
System set-up

## Slide 4
Top & bottom are bass panels
Center panels are mid/high panels
Individually driven concentric stator rings
ESL 63 construction details

## Slide 5
QUAD ESL 63
transmission line stator drive
(for 989 add two bass panels)

## Slide 6
ESL 63 stator-stator input impedance

## Slide 7
Amplifier requirements
Two opposite phase drive voltages up to 5kV pk-pk
Bridged load signal currents of up to 10mA pk-pk
Notes: There is also a more complete model that includes things like baffle step and air load mass.
Inductors are core, 2.78H (!), and are coupled with adjacent coils and damped.
The sections at the left model the high freq. sections, and at the right are the bass panels.
Bass panels have the highest capacity but are ‘ isolated’ by the transmission line sections.

## Slide 8
Design considerations – 1
  ‘Walker Equation’
Initial all-solid-state design, based on IXYZ 4.5kV FETs and IGBTs
Abandoned due to very high parasitic capacitances and small SOA

## Slide 9
Issues with HV FETs/IGBTs in linear applications
The Spirito Effect: each cell has the same gate-to-source voltage and the same capacitances but not the same gain. A higher gain cell conducts more current, causing a hotspot, leading to secondary breakdown.
High gate charge/discharge currents cause distortion.

## Slide 10
Design considerations - 2
Over to the dark side - compactron 6HS5 beam triode tubes!
+/- 2.2kV design instead of +4.4kV to limit high voltage in box
Current output into capacitive load for 1st order open loop roll off
Rely on stable NFB for lowish Zout
Monoblocs to limit cable length (capacitance)
Software safety provisions

## Slide 11
Triode/Beam Triode Common Cathode versus
Common Grid/transconductance drive

## Slide 12
Common Grid drive turns a triode into a pentode

## Slide 13
Basic output stage
Modulated current source
Next to tackle:
Floating heater & bias for top tube;
Heater & bias at -2.2kV for bottom tube

## Slide 14
Isolated heater & bias voltages

## Slide 15
Heater soft-start

## Slide 16
Linear isolated optocoupler HCNR200/TIL300
Next to tackle:
Bringing the signal to -2.2kV reference
V(R3) = Vin
V(R16) = Vin

## Slide 17
Forward audio path

## Slide 18
Output impedance (simulated)

## Slide 19
Distortion at the stators – direct drive

## Slide 20
Distortion at
the stators –
paX & Purifi

## Slide 21
Software features
Operation
Remote control
  Active/standby
  Speaker switching
Safety
At start-up: check cable connection
During operation:
  Watch cable connection
  Watch output offset
  Watch corona discharge
  … shut down if error

## Slide 22
System level
A/B drive comparison
Sources and DACs

## Slide 23
Speaker switching
Stator switching
step-up output vs. direct drive output

## Slide 24
Stator drive response matching
Stator switching step-up output vs. direct drive output

## Slide 25
System components
Source:
Volumio Primo streamer
Wireless, USB, USBstick,
HD/SSD, TIDAL
Dirac Live! room correction:
miniDSP Flex Digital
2-input 4-output DSP
DAC & EQ:
RME ADI-2 Pro Fs R
‘studio-in-a-box’, used as
Dual Stereo DAC w/ EQ

## Slide 26
DAC/EQ setup
RME ADI-2 Pro FS R in AD/DA mode used as dual DAC
  Level matching
  Response EQ on direct drive
dd eq
step-up feed
dd feed

## Slide 27
UK Patent 815.978, Walker, Peter et al, 1955
Electrostatic Loudspeakers, Peter J. Baxandall
(Chapter 3 in Loudspeaker and Headphone Handbook, John Borwick, Editor)
The Design of Electrostatic Loudspeakers, Frank Verwaal, 2017, rev 2
Any diyaudio.com thread with Bolserst, Hans Polak and Stokesd
Some further reading on ESLs
- Thanks for listening! -

## Slide 28
Questions?

## Slide 29
Audio
input
RCA
XLR
HV amp
HV amp
Symmetric signal
+5V stby
Mains
Controller
Offset
Corona
+12V SMPS
+/- 2.2kV
+/- 15V
Mains
Mains
ON/OFF
HV conn.
Stators
Cable conn.
Heaters
Bip. Sup.
HV sup.
Speaker sw.
Spkr sw.
System diagram
Sig. det.
Out
Out
ON/OFF
h/w
interlock
Sig. sel.

## Slide 30
ESL 63 transformer input impedance